## Slide 1
Intelligent Defect Detection and Preservation of Guangzhou Industrial Heritage
Buildings Based on YOLOv8 and Digital Design
Qi Duan1 ,Rui Di2,*and Weitao Pang3,Yangli Ou4
Macao Polytechnic University and Guangzhou Polytechnic University
Abstract
Guangzhou, one of China’s earliest open cities, possesses rich industrial heritage along the Pearl River. However, traditional manual surveys and expert-based assessments are inefficient, costly, and highly subjective, limiting systematic digital archiving and conservation.This study proposes an intelligent conservation framework integrating the YOLOv8 model with digital design platforms. Based on 1,521 images from industrial heritage sites along the Pearl River, a dataset covering 8 categories of building defects was constructed and used to train the YOLOv8 model.By combining YOLOv8 with BIM, Rhino, and Grasshopper, the study achieves three-dimensional visualization and dynamic management of defect information. Experimental results show a precision of 0.95, recall of 0.86, and mAP@0.5 of 0.67. Exposed reinforcement, rust stains, and tile loss demonstrate high detection accuracy, while cracks show lower precision due to fine textures and background interference.Overall, this research establishes a full-process intelligent conservation framework covering “detection–assessment–safeguarding–decision-making” and demonstrates deep integration of deep learning with digital design platforms, providing technical support for the digital and intelligent management of industrial heritage.
Objectives
To develop an intelligent framework for industrial heritage conservation by integrating YOLOv8-based defect detection with digital design platforms.
To construct a labeled dataset of typical industrial heritage defects along the Pearl River in Guangzhou and evaluate detection performance.
To achieve 3D visualization and dynamic management of defect information through BIM and Rhino–Grasshopper integration.
To support data-driven decision-making in the safeguarding and maintenance of industrial heritage buildings.
Materials & Methods
An intelligent conservation system integrating YOLOv8 and digital design platforms was developed for industrial heritage buildings. The workflow includes data acquisition, defect detection, and 3D visualization.
A dataset of 1,521 images with 8 defect categories was constructed from industrial heritage sites along the Pearl River in Guangzhou and split into training, validation, and test sets.
The YOLOv8 model was trained with an input size of 640×640 and evaluated using Precision, Recall, and mAP@0.5, with data augmentation to improve robustness.
Detection results were mapped into BIM and Rhino–Grasshopper environments to generate parametric heatmaps, enabling dynamic defect visualization and management.
Results
This study establishes an intelligent conservation framework integrating YOLOv8 with BIM and the Rhino–Grasshopper digital design platform for industrial heritage buildings along the Pearl River in Guangzhou. A dataset comprising 1,521 images and 8 typical defect categories was constructed, enabling an integrated workflow from data acquisition, model training, defect detection to 3D visualization.
Experimental results show that the YOLOv8 model achieves a precision of 0.95, recall of 0.86, mAP@0.5 of 0.67, and inference speed of 122 FPS, outperforming YOLOv5 and YOLOv7 in both accuracy and efficiency. High detection accuracy is observed for exposed reinforcement, rust stains, and tile loss, while crack defects remain challenging due to fine textures and background interference.
By mapping detection results into 3D digital models, defect heatmaps and attribute annotations are automatically generated, enabling a transition from static documentation to dynamic, data-driven heritage management.
Conlcusion
This research demonstrates that deep learning can be deeply integrated with digital design platforms to support the intelligent detection, visualization, and management of industrial heritage defects, forming a full-process framework covering “detection–assessment–safeguarding–decision-making.”
Nevertheless, limitations remain in regional generalization, sample imbalance, crack detection accuracy, and computational demands. Future work will focus on expanding multi-regional datasets, applying transfer learning, improving fine-grained crack recognition through edge enhancement and multi-modal data (e.g., infrared and point clouds), and introducing generative AI and knowledge graphs to support automatic repair prediction and decision-making, ultimately advancing a comprehensive intelligent conservation system.
References
1.Rattanapitak, W. , Khwansuwan, P. , Wangsiripitak, S. , Sirikitsathian, P. : Deep learning-based heritage building assessment with spatial context. In: IEEE 7th Symposium on Computers and Informatics (ISCI), pp. 352–357 (2025).
2.Chen, M. , Su, X. : AIGC technology driving the innovative development of ethnic minority element design in Guangxi. In: 5th International Conference on Artificial Intelligence and Industrial Technology Applications (AIITA), pp. 1647–1652 (2025).
3.Jiang, P. , Ergu, D. , Liu, F. , Cai, Y. , Ma, B. : A review of YOLO algorithm developments. Procedia Computer Science 199, 1066–1073 (2022).
4.Sohan, M. , Ram, T. S. , Reddy, C. V. R. : A review on YOLOv8 and its advancements. In: International Conference on Data Intelligence and Cognitive Informatics, pp. 529–545. Springer, Singapore (2024).
5.Szalapaj, P. : Contemporary Architecture and the Digital Design Process. Routledge, London, U. K. (2014).
6.Qiu, H. , Zhang, J. , Zhuo, L. , Xiao, Q. , Chen, Z. , Tian, H. : Research on intelligent monitoring technology for roof damage of traditional Chinese residential buildings based on improved YOLOv8: Taking ancient villages in southern Fujian as an example. Heritage Science 12(1), 231 (2024).
7.Chen, L. , Wu, L. , Wan, J. : Damage detection and digital reconstruction method for grotto murals based on YOLOv10. npj Heritage Science 13(1), 91 (2025).
8.Chen, X. , He, J. , Wang, S. : Deep learning-driven pathology detection and analysis in historic masonry buildings of Suzhou. npj Heritage Science 13(1), 197 (2025).
9.Llamas, J. , Lerones, P. M. , Medina, R. , Zalama, E. , Gómez-García-Bermejo, J. : Classification of architectural heritage images using deep learning techniques. Applied Sciences 7(10), 992 (2017).
10.Huang, W. C. , Luo, Y. S. , Liu, W. C. , Liu, H. M. : Deep learning-based crack detection on cultural heritage surfaces. Applied Sciences 15(14), 7898 (2025).
11.Xie, E. , Wang, W. , Yu, Z. , Anandkumar, A. , Alvarez, J. M. , Luo, P. : SegFormer: Simple and efficient design for semantic segmentation with transformers. Adv. Neural Inf. Process. Syst. (NeurIPS) 34, 12077–12090 (2021).
12.Gibril, M. B. A. , Al-Ruzouq, R. , Shanableh, A. , Jena, R. , Bolcek, J. , Shafri, H. Z. M. , Ghorbanzadeh, O. : Transformer-based semantic segmentation for large-scale building footprint extraction from very-high-resolution satellite images. Advances in Space Research 73(10), 4937–4954 (2024).
13.Zhang, X. , Wang, X. : Domain-adaptive organ segmentation through SegFormer architecture in clinical imaging. Transactions on Computational and Scientific Methods 5(7) (2025).
14.Zhang, Y. , Zhang, H. , Huang, Q. , Han, Y. , Zhao, M. : DsP-YOLO: An anchor-free network with DsPAN for small object detection of multiscale defects. Expert Systems with Applications 241, 122669 (2024).
15.Wu, W. , Liu, H. , Li, L. , Long, Y. , Wang, X. , Wang, Z. , Chang, Y. : Application of local fully convolutional neural network combined with YOLOv5 algorithm in small target detection of remote sensing images. PLOS One 16(10), e0259283 (2021).
16.Wei, G. , Wan, F. , Zhou, W. , Xu, C. , Ye, Z. , Liu, W. , Xu, L. : Bfd-YOLO: A YOLOv7-based detection method for building façade defects. Electronics 12(17), 3612 (2023).
17.Affes, N. , Ktari, J. , Amor, N. B. , Frikha, T. , Hamam, H. : Comparison of YOLOv5, YOLOv6, YOLOv7 and YOLOv8 for intelligent video surveillance. Journal of Information Assurance and Security 18(5) (2023).
Contact
Macao Polytechnic University, Macao, China, p2413403@mpu. edu. mo
3rd International Conference on Artificial Intelligence for Society（AIS 2026）
AIS-2629